## Slide 1: Intro. To Robotics 236927
Nemala project
Daniel Aranki
Hani Ayoub
September 2009

## Slide 2: Main idea
Map data-type
  Cell decomposition.
  Finds the path.
  Choose between two curve options when needed
    First comparison: farthest from closest obstacle
    Second comparison: starts with same orientation as current robot orientation
  Two types of paths (used for Bug Mode)
    Red: exhausted path
    Green: the rest

## Slide 3: Main idea (cont.)
Bug Mode
  Based on Bug 2
  Try:
  First bypass chance
    Choose between left\right hand side bypass
    Drive forward until no obstacle seen from relevant side sonar
  If no orthogonal green path found:
  Second bypass chance
    Keep driving forward till the robot meets the obstacle’s end
    (Then, orthogonal green path is guaranteed)

## Slide 4: Main idea (cont.)
Tuning
  First tuning
  Final tuning
Calibration
  Find global drift (Value and Direction)
  Helps driving forward and turning

## Slide 5: Difficulties and drawbacks
Slow Sonar’s response
  This disables us to continuously read sonar while driving
Inaccurate Sonar’s readings
  Deal with situation where sonar constantly read completely wrong distance
    Particle Filter does NOT help in this case
Sonar’s dynamic range is not promising in terms of lower bound (~20 cm)
The fact that only one robot is good for all.